ПРЕДМЕТ: Допуна конкурсне документације  за јавну набавку добара број 10151/2014 – Алат

Поштовани,

На основу члана 63. став 1. Закона о јавним набавкама  ("Сл.гласник РС" број  124/2012) достављамо следеће  измене конкурсне документације за јавну набавку број 10151/2014 – Алат

Допуна:

Достављамо Вам техничку спецификацију за следеће ставке:

120.Megaommetar tehnicka specifikacija: Fluke ili odgovarajuci

| Test voltage (dc) | Range (dc) | Accuracy (± reading) |
| --- | --- | --- |
| 250 V | < 200 kΩ 200 kΩ to 5 GΩ 5 GΩ to 50 GΩ > 50 GΩ | unspecified 5 % 20 % unspecified |
| 500 V | 200 kΩ 200 kΩ to 10 GΩ 10 GΩ to 100 GΩ > 100 GΩ | unspecified 5 % 20 % unspecified |
| 1000 V | < 200 kΩ 200 kΩ to 20 GΩ 20 GΩ to 200 GΩ > 200 GΩ | unspecified 5 % 20 % unspecified |
| 2500 V | < 200 kΩ 200 kΩ to 50 GΩ 50 GΩ to 500 GΩ > 500 GΩ | unspecified 5 % 20 % unspecified |
| 5000 V | < 200 kΩ 200 kΩ to 100 GΩ 100 GΩ to 1 TΩ > 1 TΩ | unspecified 5 % 20 % unspecified |
| 10000 V (1555 only) | < 200 kΩ 200 kΩ to 200 GΩ 10 GΩ to 2 TΩ > 2 TΩ | unspecified 5 % 20 % unspecified |
| Bar graph range | 0 to 1 TΩ |
| Insulation test voltage accuracy | -0 %, +10 % at 1 mA load current |
| Induced ac mains current rejection | 2 mA maximum |
| Charging rate for capacitive load | 5 seconds per μF |
| Discharge rate for capacitive load | 1.5 s/μF |
| Leakage current measurement | Range: 1 nA to 2 mA | Accuracy: ± (5 % + 2 nA) |
| Capacitance measurement | Range: 0.01 uF to 15.00 μF | Accuracy: ± (15 % rdg + 0.03 μF) |
| Timer | Range: 0 to 99 minutes | Resolution Accuracy: Setting: 1 minute Indication: 1 second |
| Live circuit warning | Warning Range: 30 V to 660 V ac/dc, 50/60 Hz | Voltage Accuracy: ± (15 % + 2 V) |

Fluke 1555 kit

- L,C,R meter   INSST9930 ili odgovarajuci                 2 kom.

• Inputs protection: 600 Vrms

• Display: 11000 counts

• Manual and Auto ranging mode

• Relative measurements

• Recording of maximum and minimum values

• Diode test under 300µA

• Continuity: rings if R< 30∧

• Hold display mode

• Auto power-off after 10 min

• Back lighting of the screen

• Shock resistant, soft moulded holster.Dim: 182x82x55mm

• CEI1010 CATIII 600V

INSST-9930 ST-9930 LCR metar

# .   Multimetar    Fluke 179/EDA2 Combo Kit – Includes Meter and Deluxe Accessories  ili odgovarajuci   ;                                                                           komada kompleta       10

| Specificacija |
| --- |
| Voltage DC | Accuracy1 | ±(0.09% + 2) |
|  | Max. resolution | 0.1 mV |
|  | Maximum | 1000 V |
| Voltage AC | Accuracy1 | ±(1.0% + 3) |
|  | Max. resolution | 0.1 mV |
|  | Maximum | 1000 V |
| Current DC | Accuracy1 | ±(1.0% + 3) |
|  | Max. resolution | 0.01 mA |
|  | Maximum | 10 A |
| Current AC | Accuracy1 | ±(1.5% + 3) |
|  | Max. resolution | 0.01 mA |
|  | Maximum | 10 A |
| Otpor | Accuracy1 | ±(0.9% + 1) |
|  | Max. resolution | 0.1 Ω |
|  | Maximum | 50 MΩ |
| Kapacitet | Accuracy1 | ±(1.2% + 2) |
|  | Max. resolution | 1 nF |
|  | Maximum | 10,000 µF |
| Frequency | Accuracy1 | ±(0.1% + 1) |
|  | Max. resolution | 0.01 Hz |
|  | Maximum | 100 kHz |
| Temperature | Accuracy1 | ±(1.0% + 10) |
|  | Max. resolution | 0.1°C |
|  | Range | -40°C / 400°C |
| Dodatna oprema | Combo Kit – Includes Meter and Deluxe Accessories |
| Garancija Neogranicena |  |
| Safety Specifications |
| Overvoltage category | EN 61010-1 to 1000 V CAT III EN 61010-1 to 600 V CAT IV |
| Agency approvals | UL, CSA, TÜV listed and VDE Pending |

Isporuciti :

- BUSS Fuse  DMM-11A                6 kom.   15.000,00

- BUSS Fuse  DMM-B-44/100        6 kom.   15.000,00

## 123.    Cropico DO 4002 ili odgovarajuci

Prenosni, precizni merač malih otpora.

- Veliki LCD displej

- Prenosna i robusna izvedba

- Baterijsko napajanje

- Merni opseg od 4 mΩ do 400 Ω (model DO 4002)

- Najbolja rezolucija 1 μΩ (model DO 4002)

- Osnovna očitana tačnost 0,05%

- 4 žična merna metoda

- Zaštita 415 Vrms

- Automatsko isključivanje instrumenta

- Garancija: 12 meseci

- Komplet sadrži:

  - Instrument  DO 4002 ili odgovarajuci

  - 4-žične merne veze

  - 5 x 1,5 V alkalne baterije

  - Uputstvo za upotrebu

  - Kalibracioni sertifikat

- Opcije:

  - 4000-01; punjive baterije i punjač

  - CB02; torbica5 x 1,5 V alkalne baterije 4000-01

  - LS03-P; merne veze dužine 3m

  - LS04-P; merne veze dužine 15m

- Amper klešta Fluke 353 ili odgovarajuce

Functions Range

Current AC/DC 0-40.00 A              1.5% ± 15 counts

0-400.0 A 	 1.5% ± 5 counts

0-2000 A; 1400 AC rms

Crest Factor

Voltage AC/DC 0-4.000 V  	1% ± 10 counts

0-40.00 V

0-400.0 V 	1% ± 5 counts

0-600 V AC rms

0-1000 V DC

Resistance         0-400.0 Ω

0-4.000 kΩ               1.5% ± 5 counts

0-40.00 kΩ

0-400.0 kΩ

Continuity beeper Appr. ≤ 30 Ω

Frequency       5.0Hz to 100.0Hz			 0.2% ± 2 counts

100.1Hz to 999Hz 		 0.5% ± 5 counts

125. Bosch Fen za vreli vazduh GHG 660 ili odgovarajuci

Bosch Fen za vreli vazduhGHG 660 LCD Professional
Nominalna snaga 2.300 W
Težina 1,0 kg
Dužina 255 mm
Visina 255 mm
Karakteristične veličine, korišćenje
Radna temperatura 50 – 660 °C
Struja vazduha 250 – 500 l/min
Bestepeno regulisanje temperature +
Stepen za hladni vazduh, 50°C +
Regulisanje vazdušne struje bestepeno

126.  ALAT HIDRAULICNI 16-300mm2 HT-300 presa za kablove ili odgovarajuca

Sila presovanja;               60 kn
  Dužina;                           460mm
  Težina;                           3,30 kg
  Opseg presovanja;            16-300mm2
  Hod klipa;                       17mm
  Pakovanje u metalnoj kutiji
  Težina kutije;                  3,30kg

130.  Duvaljka Baku BK852 ili odgovarajuce

Top of Form

Specifikacija:

- LED digitalni prikaz

- Minimalna snaga: 350W

- Protok vazduha: 0.3 to 24L/minimum

- Snaga pumpe: 45W

- Temperatura vazduha: 100℃ do 500℃

131. Baterijska lampa za glavu

Spacifikacija:

Visokokvalitetna,vodootporna lampa za glavu sa 5 LED dioda. Odeljak za baterije je smešten u zadnjem delu zbog udobnosti. Intezitet svetla: 300 Lux Dužina snopa: oko 100m Podesivi ugao lampe Do 20 sati neprekidnog rada 3x Ansmann AAA baterije

132.      Lemna stanica Weller WS81 ili ekvivalent

Specifikacija:

- Analogna lemna stanica

- Napajanje: PU 81, 80W, 230VAC

- Lemna ručka Silver Line WSP 80, 80W sa LT B vrhom

- Stalak za lemilicu KH 18

- Temperaturni opseg: 150°C - 450°C (podesiva preko potenciometra)

- ESD zaštita

- Vrhovi: LT serija vrhova

133.     Lemna stanica Weller WR2002 ili ekvivalent

Specifikacija:

- Multifunkcionalna stanica 300W / 230V

- Digitalna regulacija temperature od 50°C - 550°C

- 2 kanala

- Regulacija protoka vazduha 1 - 10l/min

- Max. vakuum 0,7bar

- Antistatik kuciste

- ECO taster za Standby rezim

Komplet sadrži:

- Napojnu jedinicu WR 2

- Lemilicu WP 80

- Odlemljivač DSX 80

- Postolje WDH 10T

- Postolje WDH 30

# 134.   Uređaj za proveru ispravnosti akumulatora DHC-RT002 ili odgovarajući  1kom

Наведенe  допуне  сматрају се саставним делом конкурсне документације за предметну јавну набавку.

комисија  за ЈН 10151/2014

______________________________

______________________________

______________________________